## Slide 1
PRESENTATION TITLE
Updated 4k recording system FPGA PCB Board Components
FPGA + Package:
Requirements: 1. XC7A series; 2. with at least 2 GTP lanes; 3. with > 120 user I/Os; 4. with >100 in stock; 5. AMD Authorized distributors; 6. as small as possible
Final Decision:
XC7A35T-2CSG325I (4GTPs, 150 user I/Os): JLCPCB, 122 in stock
Note: smaller package than 15*15 will not support enough user I/Os, 117 user I/Os needed for 8 chips in total, 4 chips can stimulate
LEDs:
1 for power, 1 for FPGA configuration status (DONE), different colors
Reference clock (For both FPGA & GTP):
Requirements: 1. differential reference clock 2. ~125MHz 3. peak-to-peak cycle-to-cycle jitter < 10ps; 4. <±20 ppm
Confirmed with Jiaao, we can have only one oscillator, and the clock management modules within the FPGA can take care of different clock domains.
Options:
Abracon AX3DCF1-125.0000T3: 125 MHz, 1.8 V, LVDS differential XO, 3.2 × 2.5 mm, ±25 ppm, 186 fs RMS phase jitter typ.
Need:
100 nF external AC-coupling capacitors;
TI LMK1D2102LRGTR: 1:2 LVDS clock buffer, 1.8 V, up to 2 GHz, ultra-low additive jitter (<60 fs RMS max), VQFN-16 (3 × 3 mm), for splitting 125 MHz clock to MGTREFCLK and MRCC.
Flash:
Requirements: 1. small size 2. 1 SPI is enough 3. Vivado can recognize 4. Artix-7 supports
Workflow: MCU → JTAG → FPGA → SPI → Flash
Options:
ISSI IS25WP128F-JKLE, 128 Mbit Serial NOR Flash, 1.65–1.95 V supply, up to 166MHz 6 × 5 mm, revision control version of IS25WP128-JKLE (used by SpikeGadget), Stock: 45 in JLCPCB, 1111 expected in Mouser on 12/16/2026 (tape-and-reel version 8000+ expected next week)
Need: Level translator, NXP NVT4858HKZ: 1.08–1.95 V A-side, 1.65–3.6 V B-side, auto-direction bidirectional level translator, up to 208 MHz, XQFN-16 (2.6 × 1.8 mm), suitable for FPGA 1.5 V  Flash 1.8 V, new version of SpikeGadget NVT4857UK
Note: Like the NVT4857UK used by SpikeGadgets, NVT4858 is originally designed for SD/SDIO memory interfaces rather than FPGA configuration flash. The voltage and speed requirements match, but boot/configuration behavior should still be validated for our design.