## Slide 1: ASIC Layout
7mm
8.1 mm
7mm
8.1 mm
512 Recording Pixels 128/512 Stimulating
PGA BUFFER SAR ADCs
PGA BUFFER SAR ADCs

## Slide 2: Bonding Map
Bonding recipe for the ASIC-board connection

## Slide 3: Chip Specifications
Gain
  Programmable 3bits: (110 – 700)
  Raw data bandwidth: (0.3Hz – 10kHz)
  Input Referred Noise: (4 – 5uVrms)
  Sampling rate: (31.25kS/s)
Stimulator
  128 channels: Compliance of +/-10V
  Resolution: 1.5uA
  Maximum Current: 22.5uA

## Slide 4: Chip Specifications
Gain
  Programmable 3bits: (110 – 700)
  Raw data bandwidth: (0.3Hz – 10kHz)
  Input Referred Noise: (4 – 5uVrms)
  Sampling rate: (31.25kS/s)
Stimulator
  128 channels: Compliance of +/-10V
  Resolution: 1.5uA
  Maximum Current: 22.5uA

## Slide 5
3.2 mm
360µn
Recording and Stimulation
Modular concept
  One module: 16 amplifiers + 4 stimulators
  Arrange 32 copies to make it 512 recording + 128 stimulators
  Programming interface programs the stimulators and the amplifiers
  The ADCs are multiplexed to 8 data lines

## Slide 6
From Pixel Input to ADC Output
  Gain: 100 – 700 (V/V)
  Bandwidth: ~0.3 Hz to 10 kHz
  IRN = 4 – 5 µVrms
  Sampling Rate: 31.25 kS/s per channel
3.2 mm
360µn
IRN (Input-Referred Noise): ~4.2 µVrms
Recording Mode

## Slide 7
Recording Mode
From Pixel Input to ADC Output
  Gain: 100 – 700 (V/V)
  Bandwidth: ~0.3 Hz to 10 kHz
  IRN = 4 – 5 µVrms
  Sampling Rate: 31.25 kS/s per channel
  DC Power: ~17.24 µW / channel
    Not including the external LDOs
3.2 mm
360µn

## Slide 8
Recording Mode
Integrated ASIC + Probe noise
µ = 6.5µVRMS and σ = 0.3µVRMS

## Slide 9: Reading Mode – How?
Custom GUI
  Recording on the top
  Stimulation on the bottom

## Slide 10: Reading Mode – How?
Custom GUI
  Recording on the top
  Stimulation on the bottom
Start recording
  Sends a sequence to FPGA to trigger the recording

## Slide 11: Reading Mode – How?
Custom GUI
  Recording on the top
  Stimulation on the bottom
Start recording
  Sends a sequence to FPGA to trigger the recording
Reset amplifier
  It sends a sequence to FPGA to trigger the reset the amplifiers

## Slide 12: Reading Mode – How?
Custom GUI
  Recording on the top
  Stimulation on the bottom
Start recording
  Sends a sequence to FPGA to trigger the recording
Reset amplifier
  It sends a sequence to FPGA to trigger the reset the amplifiers
Left and Right Gain
  They control the gains of the two sides of the chip (they can be different if needed)
  Gain will be programmed only if Program Gains is pressed

## Slide 13: What happens in the background
Recording Related Pins
  Chip_Reset: We use this pin to reset the chip to a known state
  CLK32MHz_In: If we press start recording button, the FPGA sends this clock to the ASIC to start the recording
  FE_RESET: If we press reset amplifier button, the FPGA resets the amplifiers we should see very silent channels
  Amplifier Gain: Amplifier gain is set by a Serial Peripheral Interface (SPI will talk more about this later)

## Slide 14: What happens in the background
Recording Related Pins
  Chip_Reset: We use this pin to reset the chip to a known state
  CLK32MHz_In: If we press start recording button, the FPGA sends this clock to the ASIC to start the recording
  FE_RESET: If we press reset amplifier button, the FPGA resets the amplifiers we should see very silent channels
  Amplifier Gain: Amplifier gain is set by a Serial Peripheral Interface (SPI will talk more about this later)
When recording starts: Chip will transmit these signals
  CLK32MHz_Out: Used by FPGA to readout the correct data
  Data<1:8>: Contains the recording data
    Each data line contains the information of 4 ADC (time multiplexed)
    One ADC  16amps, then 1 Data  64 amps.
  Read: Used to let the FPGA know that a new amplifier’s data is being streamed
  Sync: Used to let the FPGA know which amplifier’s data is being streamed

## Slide 15: Communication Protocol
1 Frame = 1024 clock cycles
Within each frame, there is one Sync and 16 Read
Sync, signals when the FPGA should start streaming the data  aligns the channel map
Read signals a new amplifier is being streamed
  Within each Read period, DATA streams information about 4 amplifiers (from 4 different ADCs which share the same data line)
  They all have the same location in a group of 16

## Slide 16: Communication Protocol
1 Frame = 1024 clock cycles
Within each frame, there is one Sync and 16 Read
Sync, signals when the FPGA should start streaming the data  aligns the channel map
Read signals a new amplifier is being streamed
  Within each Read period, DATA streams information about 4 amplifiers (from 4 different ADCs which share the same data line)
  They all have the same location in a group of 16

## Slide 17: Communication Protocol
1 Frame = 1024 clock cycles
Within each frame, there is one Sync and 16 Read
Sync, signals when the FPGA should start streaming the data  aligns the channel map
Read signals a new amplifier is being streamed
  Within each Read period, DATA streams information about 4 amplifiers (from 4 different ADCs which share the same data line)
  They all have the same location in a group of 16

## Slide 18: Stimulation Mode
Biphasic stimulation (monopolar/bipolar)
Fully programmable arbitrary waveform
±10V stimulation compliance
Passive charge balancing

## Slide 19: Stimulation Mode - How
Up to ~22.5µA (4-bit control) with a resolution of ~1.5 µA

## Slide 20: Stimulation Mode - How
There are 64 stimulator in each side, left and right

## Slide 21: Stimulation Mode - How
There are 64 stimulator in each side, left and right
Select the stimulator
  Fill the edge information based
  Fill the anode and cathode information
  Polarity
Stimulators can have different setting

## Slide 22: Stimulation Mode - How
There are 64 stimulator in each side, left and right
Select the stimulator
  Fill the edge information based
  Fill the anode and cathode information
  Polarity
Stimulators can have different setting

## Slide 23: Stimulation Mode - How
There are 64 stimulator in each side, left and right
Select the stimulator
  Fill the edge information based
  Fill the anode and cathode information
  Polarity
Stimulators can have different setting
Can program multiple of these stimulators at the same time

## Slide 24: Stimulation Mode - How
There are 64 stimulator in each side, left and right
Select the stimulator
  Fill the edge information based
  Fill the anode and cathode information
  Polarity
Stimulators can have different setting
Can program multiple of these stimulators at the same time
Last we select the number of pulses we want to send (1-254) and click RUN

## Slide 25: What happens in the background
Firstly, an SPI excel file is loaded to the FPGA which then sends the data to the ASIC
  The SPI has 4 data pins <CLK, L, R, LATCH>
  L and R contains information for the stimulators programming and the gain of the amplifiers.

## Slide 26: What happens in the background
Firstly, an SPI excel file is loaded to the FPGA which then sends the data to the ASIC
  The SPI has 4 data pins <CLK, L, R, LATCH>
  L and R contains information for the stimulators programming and the gain of the amplifiers.
  Another patch reads the data in these two excel files and generates the right SPI stream file that downloads to the FPGA
SPI Stream
STIM Config
Gain Config

## Slide 27: What happens in the background
Firstly, an SPI excel file is loaded to the FPGA which then sends the data to the ASIC
  The SPI has 4 data pins <CLK, L, R, LATCH>
  L and R contains information for the stimulators programming and the gain of the amplifiers.
  Another patch reads the data in these two excel files and generates the right SPI stream file that downloads to the FPGA
How does the stimulator start working?
  Firstly, we enable the stims via STIM_EN
  Then we send a short pulse to trigger the stims  STIM_START
  After 64 STIM_CLK cycles, we enable STIM_CHB which does the charge balancing

## Slide 28: Different Stim patterns each cycle?
Firstly, an SPI excel file is loaded to the FPGA which then sends the data to the ASIC
  The SPI has 4 data pins <CLK, L, R, LATCH>
  L and R contains information for the stimulators programming and the gain of the amplifiers.
  Another patch reads the data in these two excel files and generates the right SPI stream file that downloads to the FPGA
How does the stimulator start working?
  Firstly, we enable the stims via STIM_EN
  Then we send a short pulse to trigger the stims  STIM_START
  After 64 STIM_CLK cycles, we enable STIM_CHB which does the charge balancing
Different stimulation sequence is possible as long as we can generate the timing diagram shown in the right